## Slide 1
Deployment Training
X Series®
X Series Introduction
ZOLL Medical Corporation

## Slide 2
Deployment Training
X Series®
Notes: Welcome to the X Series Overview. We will start with a quick tour around the X Series followed by the everyday patient assessment functionality.

## Slide 3: Disclaimer
Subject to Medical Direction/Local Protocols
Read operator’s manual
Based upon most recent software release
Notes: These training Modules are an adjunct to formal training. You must obtain instruction from an appropriate authority before using this device for patient care. Please take some time to read the operator's manual that came with the X Series. The manual will also highlight topics not covered in these modules, such as defibrillator paddles, internal paddles and other accessories.

## Slide 4: Specifications
Small
8.9 inches x 10.4 inches x 7.9 inches or
• 22.6 cm x 20.1 cm x 26.4
cm
Light
(with battery and roll of paper)
11.7 lbs or
• 5.3 kg
Durable
Ingress Protection rating of 55
Notes: The X Series is extremely small. It’s dimensions are 8.9” x 10.4” x 7.9” (22.6 cm x 20.1 x 26.4 cm), including the handle. It is also extremely light, weighing in at only 11.7 pounds or 5.3 kg with a battery and a roll of paper.

## Slide 5: Left Side of Device
Cables and Connections
ECG Cable with 12 Lead interface
Masimo Spo2, Co-Oximetry, or Advanced Parameters
Dual Lumen or Single Lumen NIBP Hose
Oridion Micro-Stream sampling line
80mm paper roll (plain or w/grid)
Notes: All the cabling and connections on the left side of the X series have low profile connectors, making them less obtrusive and more durable. There are multiple ECG options: 3, 4, 5 and 12-lead. In addition, there is backward compatibility amongst the X Series and Propaq MD cables for ECG, temperature and IBP. . The X Series allows for standard SpO2, SpCO, SpMet, as well as advanced parameters that can include total hemoglobin (SpHb), Oxygen content (SpOC), pleth variability index (PVI), and perfusion index (PI).

## Slide 6: Right Side of Device
Connections
USB interface port for Flash/Cellular or Wifi interface
2 YSI temperature connections
3 ports for invasive pressures
Quick connect interface for Multi Function Cable
Notes: The right side of the X Series contains the ports for communications, critical care monitoring and electrical therapies, including: USB 2.0, two YSI connections are located here in the front and can be used with esophageal, rectal or surface temperature monitor probes. Three optional channels with six-pin cable connectors known as AAMI connections accept the most commonly used transducers for invasive measurement of invasive blood pressures. There is also a multi-function cable port.

## Slide 7: Back Side of Device
Features
Lithium Ion Battery with status indicators
Approximately 6 hours of continuous monitoring with fully charged battery
Auxiliary power connection for AC and DC power
Notes: At the rear of the device you can see the SurePower Battery, as well as the auxiliary power connection which can both power all of the device’s operating functions and charge the battery. There is also an embedded battery that provides a two minute buffer to change batteries or reopen a patient record. At the two minute mark, the X Series will reset to configured default settings and open a new patient record.

## Slide 8: SurePower™ Battery
SurePower™ Technology
6 hours continuous run time
Battery indicator for capacity for remaining run time at its current usage
Notes: On top is the SurePower lithium ion battery which supplies at least 6 hours continuous monitoring of ECG, pulse oximetry, capnography, 3 invasive pressure channels, 2 temperature channels, with NIBP measurements every 15 minutes and 10 defibrillation shocks at full energy at 200 joules. The SurePower Battery indicator lets you know the capacity. There is also a Battery Status Indicator on the display once powered on.

## Slide 9: Battery Status Indicator
Battery Status
Indicates approximate remaining run time
Notes: Here you can see the Battery Status Indicator, which indicates approximately how much run time remains on the battery.

## Slide 10: Battery Removal and Insertion
To remove a battery pack
Raise latch
Pull battery pack out of compartment
To install a battery pack
Line up battery at well
Push into place
Notes: To remove a battery pack, use your fingers to grasp and raise the latch and pull the battery pack out of the compartment. To install a battery pack line up the battery so it will slide into the battery well. Push the battery into place and listen for the click.

## Slide 11: Charging a Battery
SurePower™ II Battery
Charges in device
Charges in SurePower™ Battery Charger Station
Notes: The battery pack is charged in the device when it is connected to auxiliary power. In addition, it is recommended that the unit’s battery be regularly rotated into a ZOLL SurePower™ Battery Charger Station for recharging and maintenance testing.

## Slide 12: Top of Device
Visual Alarm Indicators – LED Lights
Flashing red
  High-priority patient alarm
Flashing yellow
  Low priority technical alert
Solid Green
  Moving Data
Notes: There are also LED lights on the top of the device that are visible from both the front and rear. Red, yellow, and green lights located on the top of the unit flash on and off when the unit is powered up and are used to indicate a patient alert, equipment alert, and data transfer. Flashing red means a high-priority patient alarm, flashing yellow means a medium-priority technical alert and continuous yellow low-priority technical alert.

## Slide 13: Parameter Alarm
Visual Alarm Indicators
Reveals parameter
breached
Notes: The X Series notifies the provider of a high priority alarm in a number of ways. The parameter window indicator shows the alarming parameter in red, against a white background.

## Slide 14: Audible Alarm
Audible Alarm Indicators
High-priority patient alarm
  Two sets of 5 short beeps, every 15 seconds
Medium-priority technical alert
  One set of 3 long beep tones, every 30 seconds
Notes: The X Series unit sounds an audible alarm to indicate the priority level of highest-priority active alarm. The X Series indicates the priority level using a high-priority alarm, which consists of two sets of five short beeps, every 15 seconds, a medium-priority technical alert, which is one set of 3 long beep tones, every 30 seconds and a low-priority technical alert which is a single short beep tone, not repeated.

## Slide 15: Basic Buttonology
Permanent Keys
Alarm Silence
Home
3 Navigation Keys
Snapshot
NIBP
Think:
Noise (Silence)
Needs (NIBP/Snapshot)
Navigation (Home/3 Keys)
Notes: On the front of the device you will find seven Permanent Keys down the right side (including your primary navigation keys).

## Slide 16: Basic Buttonology
Quick Access Keys
Lead View
12 Lead
Capnography
Treatment Markers
Sync Mode
Printer
More
Think:
Applications via Icons
Notes: There are seven Quick Access Soft keys down the left side. The therapy keys are located on the bottom of the X Series. Similar to other ZOLL devices, the keys are color-coded: red for defibrillation and green for pacing. Also, the steps for defibrillation are clearly labeled “1, 2 & 3” for easy, intuitive use. With these keys you can perform 80% of all device functions with no more than two button pushes from the home screen. The Electrical Therapy Keys will be reviewed in the Defibrillation, Pacing, and Synchronized Cardioversion modules.

## Slide 17: Basic Buttonology
Electrical Therapy Keys
Think:
Pacing
Cardioversion/Defibrillation
AED Function
Notes: The therapy keys are located on the bottom of the X Series. Similar to other ZOLL devices, the keys are color-coded: red for defibrillation and green for pacing. Also, the steps for defibrillation are clearly labeled “1, 2 & 3” for easy, intuitive use. With these keys you can perform 80% of all device functions with no more than two button pushes from the home screen. The Electrical Therapy Keys will be reviewed in the Defibrillation, Pacing, and Synchronized Cardioversion modules.

## Slide 18: Ready For Use Status
RFU Indicator
Status of unit
Based on most recent readiness check
“Do not use” indicator may appear as Flashing or Solid display
Notes: The ready for use (RFU) indicator can be found in the top right-hand corner of the front panel. The RFU indicator gives you an immediate indication of the X Series “readiness for use” without turning on the monitor or waiting for power up. It shows the status of the unit based on its most recent readiness check.

## Slide 19: Power Up
Check RFU symbol
Turn on device
Attach monitoring parameters to patient
Notes: Verify that the X Series defibrillator is ready for use by noting the Ready for Use symbol on the defibrillator front panel. Turn on the device so that the X Series is performing self-tests and becoming active.

## Slide 20: Noise
Alarm Reset/Alarm Suspend Key
High Priority Alarm Suspend
  90 seconds
Low Priority Alarm Silence
  Duration of encounter or until another operational alarm is triggered
Alarm reset
  Clears silenced alarm
Notes: The Alarm Reset/Suspend key both temporarily silences vital parameter alarms or acknowledges/resets functional alarms (leads off, cable off, etc.).

## Slide 21: Screen Characteristics
Date and Time
Easy to adjust
Be sure to confirm “Set Date and Time”
Notes: X Series displays the current date and time on the top left corner of the screen which is easy to see and easy to adjust. To access the Date and Time Menu, highlight the Date and Time display with Navigation Keys and press the Select Key. This can be done from the standard monitoring screen. The X Series can also be configured to Time Sync to several webservers. This configurations will allow the device to set the time and date any time the device is powered on and is connected to cellular network.

## Slide 22: Screen Characteristics
Patient Modes
Adult
Pediatric
Neonatal
Each mode will adjust to default
  Alarm settings
  NIBP Cuff Inflation Target
  Energy settings and algorithms
*Neonatal Mode has not been approved for advisory defibrillation.
Notes: The X Series offers alarm settings for Adult, Pediatric and Neonatal Modes. The latter is available only from ZOLL. You can see the indicator at the top of the screen. Each mode will adjust to default alarm settings, NIBP inflation pressures, NIBP inflation volume and initial energy settings as well as mode appropriate energy algorithms. Neonatal Mode has not been approved for advisory defibrillation.

## Slide 23: Screen Characteristics
Battery Status Indicator
Approximates remaining run time at current power consumption
Notes: Here you can see the Battery Status Indicator, which indicates approximately how much run time remains on the battery.

## Slide 24: Screen Characteristics
Elapsed Timer
Tracks elapsed time for time- critical patients
Notes: The Elapsed Timer allows you to track the elapsed time for time-critical patients.

## Slide 25: Screen Characteristics
Alert Message Bar
Vital sign alarm message
Equipment alert message
Notes: Vital sign and equipment alert messages give multiple visual indicators to make alarms easily identifiable and user-friendly. Troubleshooting is quick and easy.

## Slide 26: Permanent Keys
Display/Home Key
Toggles through 3 pre-configured screens
  Multi-channel display
  Vital trend display
  Large numeric display
Also closes any open menus
Notes: The home or display button has a dual purpose. This button allows you to scroll through the three screen modes: primary monitor multiple channel display, vital trend display and large numeric display; and closes any open (gray or sub menus) parameter windows that were opened or will return you to the primary monitor channel display.

## Slide 27: Home Key Navigation
Multi-channel Display
Display up to 4 traces
Any combination of ECG and other waveforms
Easily configurable to power up in Pads View and auto populate to a chosen Lead View upon placement of limb leads
Notes: The Multi-Channel Display is custom configurable to show up to 4 traces: any combination of ECG and physiological (EtCO2, SpO2, IBP, CPR features) waveforms can be displayed at any given time. Please click on “Multi-channel Display” link to review standard ECG monitoring for X Series.

## Slide 28: Home/Display Key
Vital Trend Display
View vital trends on screen
Provides access to print snapshots to trend screen
Notes: The Vital Trend Display Screen allows you to view all vital trends for the current patient without printing a report.

## Slide 29: Home/Display Key
Large Numeric Display
Improved visibility at greater distances
Provides a BLS view without waveforms
Notes: The Large Numeric Display gives you very large numbers for improved visibility at greater distances.

## Slide 30: Permanent Keys
Navigation Keys
3-Key Cluster
  Clockwise
  Counter clockwise
  Select
Indicator Box
  Highlighted blue box on screen display used to select parameters
If you can highlight it in blue, there is something you can do by pressing the “Select” key
Notes: The 3-key cluster of Navigation Keys to right of the screen (clockwise, counter clockwise and select) are used to move the indicator box on the screen display and to select options. The indicator box is highlighted blue.
If you can highlight it in blue, there is something you can do by pressing the “Select” key

## Slide 31: Patient Monitoring
Electrode Options
ECG electrodes
CPR Stat-padz®
Pedi-padz® II
Other therapy electrodes
Notes: The X Series cross compatibility with CPR Stat-padz®, Pedi-padz® II, ECG Electrodes, and other therapy electrodes. For more information consult the X Series Operator Guide.

## Slide 32: Patient Monitoring
ECG Lead Configurations
3-lead
4-lead
5-lead
12-lead
Notes: The X Series can monitor the electrocardiogram with the following configurations: 3-lead, 4–lead, 5-lead or 12-lead.
The X Series offers a monitoring display of up to four different waveforms. 12-lead ECG Monitoring is also available, which provides simultaneous acquisition and storage of 12-lead information. The device is capable of monitoring all 12 leads. A static 12-lead (resting ECG) is easily acquired.

## Slide 33: Primary Lead Default
Configurable Auto-Populate Feature
Pad View displays on power up and populates Source Lead View channel if pads applied to patient
If standard ECG monitoring electrodes are applied instead – a preselected lead view will populate the Source Lead View channel automatically
Notes: The X Series when configured will power up in Pad view. This allows the provider an immediate pad view. Should the Pads not be used and standard ECG monitoring leads applied, the X Series will automatically change to a pre configured selected lead view.

## Slide 34: Respirations
Impedance Pneumography
Monitors respirations through changes in thoracic impedance
Uses standard ECG cable
Provides respiratory rate without use of additional adaptors or cables
Notes: The x series can be configured to monitor respiration via impedance pneumography technology, which means that breaths are measured through changes in thoracic impedance. A standard ECG lead cable is used (Leads I or II), so no additional adapters or cables are necessary. The X Series automatically transitions from pneumography to capnography when the latter is activated.

## Slide 35: CO-Oximetry
Monitoring CO-Oximetry
SpO2, SpCO® and SpMet®
Foot, toe, or finger sites
SpCO and SpMet are optional features
Masimo, Rainbow, SET, SpCO, and SpMet are trademarks or registered trademarks of Masimo Corporation.
Notes: The X Series CO-Oximeter continuously and noninvasively measures the oxygen saturation of arterial hemoglobin (SpO2), carboxyhemoglobin saturation (SpCO), and methemoglobin saturation (SpMet) at a peripheral site, such as the finger, foot, toe or ear. New Advanced Parameters can also include the following :Total Hemoglobin(SpHb), Oxygen Content (SpOC), Pleth Variability Index (PVI),Perfusion Index (PI). This monitoring gives information about the cardiac and respiratory systems, perfusion details and provides details of oxygen transportation in the body.

## Slide 36: CO-Oximetry Cable
CO-Oximetry Cable Connection
Intended for use with Masimo® Rainbow® SET sensors
Once signal is acquired plethysmograph will auto populate into waveform channel
Notes: The X Series CO-Oximetry and advanced parameter (SpHb) options are intended for use only with with Masimo Rainbow SET sensors. The CO-Oximetry sensor contains light-emitting diodes (LEDs) that transmit various visible and infrared light through the body’s extremities. The transmitted light is then received by a photodetector, which converts it to an electronic signal. The signal is then sent to the X Series unit for processing.

## Slide 37: CO-Oximetry
CO-Oximetry Display
Pulse bar
Large numeric format of SpO2 value
SpCO and SpMet values will alternate
Notes: Pulse oximetry measurements begin as soon as the sensor is applied to the patient and connected to the X Series unit. The X Series displays SpO2 values and pulse bar in a large numeric format, with additional CO-Oximetry options automatically scrolling in the lower portion of the SpO2 window. This eliminates the need for users to request information increasing ease of use. The CO-Oximetry probe requires only one calibration per use – at power up, as opposed to recalibrating at each transition between functions. If SpCO and SpMet are installed, the SpCO and SpMet measurements will alternate every two seconds underneath the SpO2 display.

## Slide 38: Advanced Parameter Monitoring
    SpHb*: Total Hemoglobin
        Track changes in hemoglobin
          Does my patient need blood?
    SpOC*: Total Arterial Oxygen Content
        Measurement factors both SpO2 and Hb together providing a combined assessment in quick, automated, continuous manner
          What’s my patient’s true oxygenation status?
    PVI*: Pleth Variability Index
        Fluid Status assessment
          Will my patient respond to fluid?
    PI*: Perfusion Index
        Quality of monitoring site?
          How well is my patient really perfusing peripherally?
Masimo, Rainbow, SET, SpHb, SpOC, PVI, and PI are trademarks or registered trademarks of Masimo Corporation.
Notes: Additional critical care monitoring is available with SpHb sensor. If SpCO and SpMet, or SpHb, SpOC, PVI and PI are installed and monitoring is on for these parameters, the measurements will alternate every two seconds underneath the display.

## Slide 39: Permanent Keys
Snapshot Key
Captures 24 seconds of data
  12 seconds prior
  12 seconds after
Option to print on activation
  Stores temporarily to Trend Display for single snapshot print capability
  Stores to printable Treatment Summary Report
Notes: Pushing the Snapshot Key represents midpoint of a 24 second snapshot: a total of 24 seconds of data is captured – 12 seconds prior and 12 seconds after the key press.

## Slide 40: Permanent Keys
NIBP Key
Initiates or aborts a blood pressure measurement
When obtaining NIBP
  Right size
  Right Placement
  As close to skin as possible
Notes: The NIBP Key initiates or aborts a single blood pressure assessment. Click on NIBP Key link to review the NIBP module.

## Slide 41: Quick Access Keys
Quick Access Key Levels
First level keys
Second level keys
ICON represents associated application
Notes: You can access the X Series functions using the quick access keys that are located on the left side of the display screen. When you press the last key, the left arrow, five more keys are displayed.

## Slide 42: Quick Access Keys (First Group)
Lead Select Key
Changes primary monitoring lead
Notes: The Lead Select Key allows you to change the monitoring lead quickly. To learn more about ECG Monitoring, review the ECG Monitoring module.

## Slide 43: Quick Access Keys (First Group)
12-Lead Key
Accesses 12-Lead monitoring menu
Notes: The 12-Lead Key accesses the X Series 12-Lead monitoring capabilities. More detailed information will be reviewed in the ECG Monitoring Module. Click on the 12 Lead Key link to review 12 Lead Acquisition.

## Slide 44: Quick Access Keys (First Group)
CO2 Key
Activates and deactivates capnography
Insert sampling adjunct
Turn ON
Attach to patient
Notes: The CO2 Key activates or deactivates capnography. Click on link to review the Capnography Module.

## Slide 45: Quick Access Keys (First Group)
Treatment Key
Formally known as Code Markers
Multiple options
Custom configurable
Records 6 seconds prior and 8 seconds post selection
Records to Treatment Summary
Notes: The Treatment Key initiates what we have historically called Code Markers. The Treatment Markers provide multiple options: 2 pages with 5 options per page, and are custom configurable. Treatment markers must be preconfigured in the Supervisor Menu. When preconfiguring, select from a preset list or manually enter any label.

## Slide 46: Quick Access Keys (First Group)
Printer Key
Can be activated and stopped any time
Provider determines length of strip
Does not record to printable memory
Notes: The Printer or Recorder Key either starts or stops the printer, allowing you to determine how long a strip you need for any given situation. The X Series offers 80mm plain white with an option to print the grid, or pre-printed red grid paper.

## Slide 47: Quick Access Keys (Second Group)
Brightness Key
Standard color display
High contrast with white background
Night-vision goggle-friendly mode (optional)
Notes: The Brightness Key also offers three functional screen modes: color, high contrast with a white background and night-vision goggle-friendly mode when configured.

## Slide 48: Quick Access Keys (Second Group)
IBP Key
Accesses IBP menu
Notes: The IBP Quick Access Key allows you to access the IBP Menu in the critical care versions of the X Series. Click on IBP Key link to learn more about IBP.

## Slide 49: Quick Access Keys (Second Group)
Alarm Menu Key
Accesses alarm quick access menu keys
  Stat Set Key
  Alarm Suspend Key
  Alarm Limits Key
Notes: Pressing the Alarm Menu Key provides access to all alarm functions.

## Slide 50: Quick Access Keys (Second Group)
Log Key
Treatment Summary Report
Print Trends
Trend Format Display
USB Case Upload
Case Push
Notes: X Series has a vast data storage capacity, which can be accessed by pressing the Log Menu Key. To learn more about the Log menu, please open link to review the Communication and Data module.

## Slide 51: Quick Access Keys (Second Group)
Setup Menu Key
Change minor configuration options
Run operational tests
Supervisor menu
Notes: The Setup Menu Key allows the user to change minor configuration options related to ECG, display, volume, printer and trends. The menu also allows the user to run tests on specific operational functions. There is a Supervisor Menu as well, which is password-protected since it allows changes to many of the major configurations.

## Slide 52: Quick Access Keys (Second Group)
More/Back Key
Toggles between two pages of Quick Access Keys
Backs out of Quick Access Menus
Notes: The More/Back Key allows you to toggle between 2 pages of Quick Access Keys. It also allows you to back out of the Quick Access Menus altogether.

## Slide 53: Energy Features
Hands-Free Therapy Cables
Quick-disconnect Multi-Function cable
Standard ZOLL MFC connection
Notes: The X Series is compatible with a number of cables for defibrillation. The “quick-disconnect” multi-function defibrillation/pacing cable is used for monitoring, as well as delivery of therapy such as defibrillation, cardioversion and pacing. The connector on the multi-function cable allows for backward compatibility with all ZOLL electrodes.

## Slide 54: Preparation
Readiness Plan
Place X Series next to patient
Check RFU symbol
Turn on device
Open or remove shirt
Attach therapy electrodes
Notes: Place the X Series next to the patient. Verify that the X Series defibrillator is ready for use by noting the Ready for Use symbol on the defibrillator front panel. Turn on the device so that the X Series is performing self-tests and becoming active. Open or remove the patient’s shirt and attach therapy electrodes.

## Slide 55: Synchronized Cardioversion
Sync Key
Activates and deactivates synchronized cardioversion
Denotes R Wave with yellow dot
Confirms sync mode with “S” above every R wave recognition
Notes: The Sync Key synchronizes with R Wave on patient’s ECG signal in order to deliver synchronized cardioversion. It’s location on the screen at power up allows for quick, easy access when needed. Click on link to review the Synchronized Cardioversion Module.

## Slide 56: Defibrillation
X Series Defibrillation Options
AED Mode
Manual Mode with Advisory/CPR Protocol
Emergency defibrillation
Always follow local protocols
Notes: The X Series can deliver defibrillation in a number of ways. In this module, we will highlight how to use the X Series in the AED Mode. We will also review how to use the Manual Mode with an Advisory/CPR Protocol set-up and how to use the X Series to deliver emergency defibrillation. We will review these modes with the use of hands-free therapy electrodes for defibrillation throughout this module. Defibrillation with internal and external paddles will not be reviewed. Always follow your local resuscitation protocols.

## Slide 57: Pacing
Pacer
  Initiates Pacing Dashboard
  Configurable to Demand or Fixed Pacing Mode
  Output starts at 30 mA
Notes: The X Series provides state the art pacing technology allowing capture at lower outputs thereby reducing patient discomfort. Click on Pacer Link to review detailed Pacer functionality.

## Slide 58: CPR Dashboard
Compression Bars
A bar for each compression
Top line is baseline
First dotted line 2 inches (5 centimeters)
Second dotted line 2.4 inches (6 centimeters)
Notes: Once the X Series is connected to a defibrillation electrodes with the CPR sensor, the CPR Dashboard will automatically appear after 5-8 compressions. On the CPR Dashboard display you have several critical items which will allow you to obtain real-time CPR feedback. First you will notice a bar representing each compression. The top solid line represents the baseline. The first dotted line represents 2.0 inches (5 centimeters) and the second 2.4 inches (6 centimeters). Keeping the bar within the dotted lines lets you know that your depth is correct and within the current Guidelines of at least 2 inches (5 centimeters).

## Slide 59: CPR Dashboard
Depth and Rate
Instantaneous values
Color of value changes when outside recommendations
  Green values = within recommendations
  Yellow values = outside recommendations
Notes: You will also notice numeric readings of depth and rate to further assist you in meeting the new AHA/ERC Guidelines. What better way is there for you to know that you are compressing at a rate of at least 100 compressions per minute and/or a depth of at least 2 inches (5 centimeters) than seeing a “100” and a “2” on the screen. You will also notice that the values change color when outside of Guideline recommendations.

## Slide 60: CPR Dashboard
Release Indicator
Tracks if you fully come off the chest
Bar full = full recoil
FULLY RELEASE text prompt is not
a default setting
Notes: Next you will see a Release Indicator, which lets you know whether or not you have come fully off the chest. When the bar is full, you have allowed for full recoil.
The X Series unit can be configured to display the text prompt FULLY RELEASE, which instructs rescuers to lift their hands from the patient’s chest after compressions to allow full recoil. This prompt occurs 45 seconds into the CPR interval. By default, the FULLY RELEASE text prompt is not enabled.

## Slide 61: CPR Dashboard
Chest Compression Indicator
Indicates rate and depth are within current guidelines
Keep shape full
Notes: This diamond-shaped figure provides a quick, overall indicator of how well the rescuer's
combined rate and depth of chest compressions match the AHA/ERC recommendations for
adult CPR.
The CPR Compression Indicator, also known as Perfusion Performance Indicator (PPI), is first
displayed as an empty diamond. This indicator starts to fill as compressions begin (filling from
the inside), and becomes completely filled when consistent chest compression depth exceeding
AHA/ERC 2010: 2.0 inches and rate exceeding 90 compressions per minute (cpm) are achieved simultaneously. The CCI also gives you an excellent indication of the detrimental impact of pausing: as soon as you stop compression, the shape empties quickly. Some describe this phenomenon as being like “air” coming out of a “leaky balloon”.

## Slide 62: CPR Dashboard
CPR Timer/Idle Timer
Counts down 2 minutes during CPR
Becomes Idle Timer when there is a pause in CPR
Notes: Above the CCI you will see the CPR Timer, which counts down 2 minutes, letting you know how much time remains before pausing to verify the rhythm and shock, if necessary. When CPR is paused, the CPR Timer quickly becomes an Idle Timer, which let you know how long the patient has been without blood flow. The idle timer will start after 10 seconds of no compressions.

## Slide 63: CPR Feedback
CPR Voice Prompts
“Push Harder”
“Good Compressions”
Voice prompts are not default settings
Notes: The X Series unit can be configured to issue voice prompts related to the depth of chest compressions as feedback to rescuers performing CPR. Two voice prompts are available for
this purpose: Push Harder and Good Compressions. This is not a default setting. When chest compressions are detected but their depth is consistently less than the target depth the device periodically issues the “Push Harder” voice prompt. If the rescuer responds by increasing compression depth to more than the target depth on a consistent basis, the unit issues a “Good Compressions” prompt.

## Slide 64: CPR Feedback
CPR Metronome
Beep for compression rhythm to follow
Silent when chest compressions stop being detected
Notes: The X Series unit includes a CPR metronome feature that can be used to encourage rescuers to perform chest compressions at the AHA/ERC recommended rate of 100 compressions per minute. This metronome can be configured to operate in both AED and Manual Modes, or in AED Mode only. It can also be disabled for all Modes.
When activated, the metronome beeps at the AHA/ERC recommended rate to provide a compression rhythm for rescuers to follow. The metronome is silent when chest compressions stop being detected by CPR-equipped hands-free therapy electrodes.

## Slide 65: See-Thru CPR®
Filtered ECG
Filters out compression artifact
Picture of underlying heart rhythm without stopping CPR
Filtered ECG is below the top trace
Filtered ECG may be configured to automatically populate once CPR is initiated when utilizing CPR Stat Padz
Notes: X Series has See-Thru CPR, an amazing technology available only from ZOLL. See-Thru CPR filters out the compression artifact, allowing you to get a picture of the underlying heart rhythm without stopping CPR. You can see the top trace is the ECG with artifact. Immediately below, where it says “Filt. ECG” is the view of what’s going on under all that noise. At the end of the 2 minutes of CPR, you still have to verify the rhythm before determining whether or not a shock is necessary, but See-Thru CPR has given you a pretty good idea about what is going on so the duration of the pauses will likely be minimized. As the AHA/ERC Guidelines emphasize, minimizing pause time can decrease hands off time. The filtered ECG may be configured to automatically populate once CPR initiated using CPR Stat Padz.

## Slide 66
Thank you
Notes: You have reached the end of the X Series Deployment Training.

## Slide 67: Success!
C ON GR AT U L AT ION S
You have reached the end of the X Series Deployment Training
Notes: You have reached the end of the X Series Deployment Training.